## Slide 1: H3drv homework (RZ+SL)
12.6.2023
RZ, SL
Notes: v1.1: added slides for ppt (SL, 5.6.23)
v1.0: first version with basic structure (SL, 30.5.23)

## Slide 2: H3drv homework - agenda
Goal
Setup
Theory
MCC-H3 prj
Findings
Authors
  reiner.zieglmeier@microchip.com
  stefan.luethin@microchip.com

## Slide 3: Goal

## Slide 4: H3drv homework: goal
QT8-touch
clickTouch
I2C
UART
PC
python
x,y
moveMouseOnScreen -> winLib see last slide
analyzing x,y-inputs and maybe FFT over it, we could maybe detect a button-press and with python then indicate this - eg: different icon, like filled-hand vs not-filled-hand that just moves
comm to sensor
initSens()
  initTouch()
  initQT8()
readSens() -> call on if flag=set / flag set in ISR
  rdTouch()
  rdQT8()
  extractXY()
sendToHost()
  ...
#eof
use H3-modules
console (UART,USB)
  mcuOutPos(X,Y)
debug
  ??needed?
cmdIF
  mcuInSens() -> change activeSensor
  #eof
simulate mouse and animation x,y
init() -> selectIcon()
  read icon, eg: mouse, that will be moved on screen
getXY()
  just read from keyboard in v1
  will come from MCU/realSensor later in v2
moveIcon(x,y)
  use winCalls (last slide) to move icon
  #eof
PTC
getXY()
sendToHost(x,y)
MCU/H3
x: ... / y: ...

## Slide 5: Setup

## Slide 6: H3drv homework: setup
Setup step
  MPLABX -> chaos/nightmare (still ongoing) with v6.10 vs v6.05
  git-repo
    git-account -> create git-repo and invite collaborators
    git-bash & SourceTree
    Work-flow, branches…
  Harmony3-repos
    Which repos are needed and how to fetch and/or update -> use MCC-CM
    BUT due to current problems with MCC-CM stick to old MHC3-CM or git-bash
    need to install git.exe AND old HMC3-CM plugin doesn’t show up in MPLABX-plugins-available -> need to do manually
    runme.bat just pops up a dos-shell and disappears, why? Well runme.bat needs ‘java.exe’ in path…
    Finally MHC3-CM is up and now can setup your H3-repos
  Create initial H3-prj -> see ‘part: touchClick’
    Where to start? MHC3 vs MCC-H3 (see later slides)
  Steps to create final goal
    How to break it down
    How to org parallel development

## Slide 7: H3drv homework: setup
Used env:
Use H3-plib and -drv to access two different touch-solutions with SAMC21J18a
  QT8 -> requires PTC-peripheral
  mikroE touch-click-1995 with ‘MTCH6102’ -> required I2C-peripheral
Physical setup on the right
Environment
  MPLABX-v6.05
  XC32-v4.21
  DFP-3.8.119, CMSIS-5.8.0
  MCC-H3 repos used:
    csp-v3.16.0, core-v3.12.0,
    content-manager
hide

## Slide 8: Theory

## Slide 9: H3drv homework: theory
…
REINER
Theorie

## Slide 10: MCC-H3 project
SAMC21J18a with
a) touch-1995 click (I2C)
b) QT8-xpl (PTC)
HIDE

## Slide 11: H3drv homework: concept
concept
  Start with baseline-prj = MCC-H3 prj for SAMC21J18a with
    only STDIO+SERCOM=printf()
  Then work on tree git-branches
    B1: baseline + click touch-1995
    B2: baseline + QT8
    ->merge1: have both touch-solution and select with static-bool
    B3: H3-console
    ->merge2: replace STDIO/printf() in B2 with H3-console
    B4: H3-cmdIF, so we can switch between touch1/2 from ext-command (eg: python-script)
    ->merge3: B3 + H3-cmdIF
    …
Baseline: MCCH3 for SAMC21 with STDIO -> printf() (=> git-tag x???x )
Touch-1995 click
(=> git-tag x???x )
QT8
(=> git-tag x???x )
H3_console (=> git-tag x???x )
B1
B2
B3
merge1
merge2
B4
H3_cmdIF (=> git-tag x???x )
merge3
HIDE

## Slide 12: H3drv homework/b1: MCC-prj for click
Part1: step-by-step guidance for SAMC21J18a + mikroE-click touch-1995 on EXT3

## Slide 13: H3drv homework/b1: MCC-prj for click
B1: touchClick – step1a: h3-prj on PLIB->DRV-level to access thermo5Click on I2C
  Start: DEV7/PLIB Lab1: reads Temp from IOxpl and outputs via UART, but on SAMD21 with challenges
  Next port DEV8/DRV Lab1 = DEV7/L1 but DRV-level and on SAME54 -> port to SAMC21 more challenges
  Adding SW0
    Added SW0 to only UARTprint if SW=pressed
    BUT SW not working, why? -> click on EXT3 connected, but EXT3 pins collide with SW0…
    removing EXT3 board, SW worked immediately
  Replacing IOxpl-tempSens with thermo5Click
    IOxpl-tempSens stores T as 2B@oneAddr -> 1x I2C_WrRd()
    Thermo5-click stores T as 1B@twoAddr -> 2x I2C_WrRd()
  Replacing SW0 with touchButton
    … (inWork)
  Replacing thermo5 with touchClick
    … (inWork)
SAMC21
SPI/I2C
goal
SAMC21
SPI/I2C
State-of-today
Step1b: thermo5 + SW0
Step1c: SW0 -> touchButton
Step1a: H3-DRV prj

## Slide 14: H3drv homework/b2: MCC-prj for click
Branch2: QT8-xpl on EXT1 - Step1: start from Atmel-START prj
in A-START: create Atmel-START prj and make sure it compiles ok
in A-START: export A-Start prj
in MPLABX: import into MPLABX
in MPLABX: fix
  libraries are not added to prj -> manually add tx-libs in prj-view
  adjust #include-paths (??)
download+run ok?
START-prj ->hide

## Slide 15: H3drv homework/b2: MCC-prj for click
Step-by-step guidance for SAMC21J18a with Touch2 = QT8-xpl on EXT1

## Slide 16: H3drv homework/b2: MCC-prj for click
Branch2: QT8-xpl on EXT1 – Step2: create with MCC-H3 with same result BUT created with MCC-H3 from scratch
…
REINER
Prj QT8+python

## Slide 17: Touch Configurator – Sensor /Pin Selection
The kit has a 5x5 2D Touch Surface sensor and driven shield.

## Slide 18: Findings
Finding during H3-usage

## Slide 19: H3drv homework: findings
Findings part1: setup+touchClick
  MPLABX
    MPLABX-v6.10 screws up v6.05
    MPLABX-exceptions
  MCC-CM not stable -> only stable way still
    Use old MHC3-CM or git-bash or …
    AND make sure on MCC-CM start ‘all required content is available…’
    Set H3-path + ‘always ask’ flag
    Default settings ‘File Handling’ deletes you app*.c/h ->not clear yet why, when..

## Slide 20: H3drv homework: findings
Findings part1: touchClick (continued)
  MCC-H3 confusing tool structure – eg:
    Start/stop MCC-H3 from three different places
    H3-addOn-managers (where are they?)
    How to GenerateCode?

## Slide 21: H3drv homework: findings
Findings part1: touchClick (continued)
  Documentation -> Docu: hyperlinks missing in online-PLIB-doc and cannot filter on left or enlarge window ->usability

## Slide 22: Thank You

## Slide 23: H3drv homework/m1: both touch
Merge branch1/click-touch with branch2/qt8-touch
In work

## Slide 24: H3drv homework: findings
Findings part1: touchClick (SL)
  MPLABX-v6.10 screws up v6.05
  MPLABX-exceptions
  MCC-CM not stable -> only stable way still
    Use old MHC3-CM or git-bash or …
    AND make sure on MCC-CM start ‘all required content is available…’
    Set H3-path + ‘always ask’ flag
Keep&hide

## Slide 25: H3drv homework: findings
Findings part1: touchClick
  MCC-Structure
    MCC-plugin -> MCC-core-> Harmony-core way to complex…
    Must be online to start MCC (if Harmony-core not matching…)
    …
Keep&hide

## Slide 26: H3drv homework: findings
Findings part1: touchClick (continued)
  Porting between versions
    Old MHC3 -> stored config in 2 files harmony.prj + <h3config>.xml in ‘firmware\src\config\<h3config>\’ ->opening oldMHC3-prj with latest MCC shows 2 pops and converts h3config into one file ‘firmware\prj.X\*.mc3’ => even if converted to MCCH3-mc3 file, you still get these popups did something go wrong? No, must manually remove old-MHC3cfg ‘*.prj + *.xml’
    Last MHC3 stores config in one directory ‘firmware\src\config\<h3config>\<h3config>.mhc\*.yml’ ->porting this to MCC-H3 converts all into *.mc3 AND places a ‘mcc.txt’ into <h3config>.mhc\ that says ‘mcc convert success’ ->but porting from lateMHC3 to MCC, but on first conversion as it doesn’t know any of the prj-files, hence lots of merge-issues and if haven’t seen microchipdeveloper/port-mhc-2-mcc might completely ruin your sources
    Porting from D21 -> C21 (same arch = easy?!?!)
      Change MCU in MPLABX-prjProp -> start MCC
      MCC detects new arch and offers with popup to port BUT clock connected on GCLK1 is left open, hence no cpu-clock…
hide